## Slide 1: MICROCONTROLLERS PROJECT THERMOSTAT CIRCUIT DESIGN

## Slide 2: 1.Block Scheme
Microcontroller
Temperature Sensor
Display
Keyboard
Execution Element

## Slide 3: 2.The temperature sensor
To restrain the area for finding the perfect resistor for my thermostat I will use an analog temperature sensor. Why an analog sensor? Because analog sensor are easier to use, they have a faster response time and have a lower cost. The signal at the output of the sensor is continuous and directly proportional to the temperature.
Next, I will briefly explain the 4 categories of analog temperature sensors.

## Slide 4: 2.1. Analog temperature sensors categories
2.1.1. Thermistors
Thermistors are made of semiconductor materials and their resistance changes with temperature. There are two types of thermistors, NTC(Negative Temperature Coefficient – the resistance decreases as temperature increases) and PTC(Positive Temperature Coefficient - resistance increases as temperature increases).
2.1.2. Thermocouples
Thermocouples are made of two different metals joined together these metals is heated or cooled, they generate a small voltage (called the Seebeck effect), which is proportional to the temperature.
2.1.3. RTDs (Resistance Temperature Detectors)
RTDs measure temperature by correlating the resistance of a metal (usually platinum) with temperature. As temperature increases, the resistance of the metal increases in a predictable way.
2.1.4. Analog Output IC Sensors
These are integrated circuits (ICs) that measure temperature and provide a linear analog output (voltage or current) proportional to the temperature. They often include built-in signal conditioning.

## Slide 5: 2.2. The chosen sensors
2.2.1. LMT70
precision ±0.2°C (max)
range: -20°C to 90°C
power supply current: 9.2 µA (typ)12 µA (max)
size: 0.88 mm by 0.88 mm
already calibrated for °C
Price: 12 dollars a piece
needs amplifier because of low output voltage
2.2.2. YSI 44031
precision ±0.1°C (max)
range: 0°C to 70°C
high sensitivity
size: 0.095″ (2.4 mm) Maximum Diameter
Price: 16 dollars a piece
needs special calibration
output is not linear
2.2.3. LM35
precision ±0.5°C (max)
range: -55°C to 150°C
power supply current: less than 60A
widely available
already calibrated for °C
Price: 1 dollar a piece
outputs a linear analog voltage (10mV per °C).

## Slide 6: 2.3. The sensor for the thermostat.
Between these three resistors that I picked, the LMT70 is the best choice for my project. It has both the range and precision, it is already calibrated and it is very small. The YSI 44031 thermistor is also a really good choice, but these two have something in common that is crucial for my project. Both of them don’t exist in Proteus 8 library, and because that is the program required for the project I will have to pick LM35. In my thermostat I really want to use a Analogic IC sensor for its simplicity, so the LM35 is the next best choice after LMT70. I know that it doesn’t meet the specification but in the datasheet is specified that at room temperature it has a precision of ±0.25°C, so that sure helps.